## Slide 1: MECH 5970/6970
Lectures on Vision-based Navigation and Guidance
Sridhar Lakshmanan
Electrical & Computer Engineering
University of Michigan-Dearborn
Email: Lakshman@umich.edu

## Slide 2: Why vision-based navigation?
Navigation in GPS-denied environments
  Unintentional – e.g., ionospheric, buildings, wide-band interference
  Intentional – e.g., jamming, spoofing, damage to satellites/relay-stations
  Indoor, Underwater, Tunnels, …
Navigation in poor INS sensor performance – bias, drift, scaling, …

## Slide 3: Fundamentals of vision-based navigation
Identify fixed points in the world over two successive image frames
  Correspondence problem
Estimate the camera’s translation and rotation from these points
  Inverse problem

## Slide 4: Correspondence problem

## Slide 5: 3-steps to solving correspondence
Find interest points in both image
  Corners, blobs, T-junctions
  Needs to be repeatable – under different viewing conditions
Find descriptor for interest points
  Distinct feature vector
  Robust to noise, detection errors, geometric/photometric distortions
Match descriptors between the two images
  Distance-based: Euclidean, Mahalanobis, …
Compromise needed between feature vector dimension, distinctness, robustness and matching complexity

## Slide 6: Finding interest points
Need a method for detecting all types interest points and at any scale
Image
Gaussian kernel 
Width determined by  
Larger  implies more smoothing of I
Scale-space representation of I
Scale-normalized representation of I

## Slide 7: Extrema of D  point of interest
Increasing scale  decreasing image detail
(x,y,) is point of interest if it is a DOG extrema

## Slide 8: Matlab examples
Gaussian pyramid
Difference of Gaussian Pyramid
Interest point detector

## Slide 9: Descriptor of interest point
For each interest point (x*,y*,*), in a spatial window around (x*,y*), compute gradient magnitude and direction using the Gaussian smoothed image L(.,.) corresponding to *
’s
Interest point descriptor based on 2x2 histograms of
H11(x*,y*)
H12(x*,y*)
H22(x*,y*)
H21(x*,y*)

## Slide 10: Matching of interest points
Minimum Euclidean distance:
For each interest point (x*,y*) at t0, find , where the minimum is only over the interest points (,) at t1.
References:
(Correspondence Problem)
T. Lindberg, “Feature Detection with Automatic Scale Selection,” Int. J. of Computer Vision, 1998
D.G. Lowe, “Distinctive Image Features from Scale-Invariant Keypoints,” INTERNATIONAL JOURNAL OF COMPUTER VISION, 2004
H. Bay, et. al., “SURF: Speeded Up Robust Features,” Journal Computer Vision and Image Understanding, 2008
(Inverse Problem)
M.K. Kaiser, et. al., “Vision-Based Estimation for Guidance, Navigation, and Control of an Aerial Vehicle,” IEEE TRANSACTIONS ON AEROSPACE AND ELECTRONIC SYSTEMS, 2010
(Building Rome from 2 million Flickr images in a day)
https://grail.cs.washington.edu/rome/

## Slide 11: Matlab examples
Feature extractor
Feature matching

## Slide 12: Homework (Due 9/27/2019)
Problem 1
Consider the ‘detectSURFFeatures’ call. By changing the ‘MetricThreshold’ input argument, one can generate more/less points of interest. Plot number of detected features vs MetricThreshold value
Problem 2
Consider the ‘matchFeatures’ call -
  by changing the ‘MatchThreshold’ input argument, one can generate more/less matches between the images. Plot number of matched features vs MatchThreshold value
  By changing the ‘MaxRatio’ input argument, one can also can generate more/less matches between the images. Plot number of matched features vs MaxRatio value
Problem 3
Consider the two images ‘reference_map.jpg’ and ‘‘img_132.png’. Optimally select all the input parameters in the detectSURFFeatures and matchFeatures calls, so that at least 20 interest points are matched between them
Problem 4 (Extra credit)
Repeat Problem 3 for ‘reference_map.jpg’ and ‘test-image.jpg’